## Slide 1: Neural Audio Codec: Recent Progress and a Case Study with SemantiCodec
Wenwu Wang
Centre for Vision, Speech and Signal Processing (CVSSP)
University of Surrey
Joint work with Haohe Liu, Xuenan Xu, Yi Yuan, Mengyue Wu, Mark D. Plumbley

## Slide 2
Outline
Background: Audio Codec & Neural Audio Codec
Motivation: Limitations with Current Neural Codecs
Proposed Method: SemantiCodec
Experimental Results:
Conclusions and Future Works

## Slide 3: Audio Codec
A device or software that encodes or decodes digital audio data for transmission, storage, or playback.
Compressor-decompressor  “Codec”
MP3, FLAC, AAC, Vorbis, etc.

## Slide 4: Neural Audio Codec
SoundStream (Zeghidour et al. 2021)
Encodec (Défossez et al. 2021)
Descript (Kumar et al. 2023)
HiFi-Codec (Yang et al. 2023)
SpeechTokenizer (Zhang et al, 2023)
Codec Superb Benchmark (Wu et al. 2024)
  https://github.com/voidful/Codec-SUPERB

## Slide 5: Beyond Communication
AudioGen (Kreuk et al. 2022), AudioLM (Borsos et al. 2023), MusicLM (Agostinelli et al. 2023), MusicGen (Copet et al. 2024)
VALL-E (Wang et al. 2023), XTTS (Casanova et al. 2024)
FlashSpeech (Ye et al. 2024), NaturalSpeech 3 (Ju et al. 2024)
Used as tokenizer of audio (AR modeling), or the latent representation of audio (Diffusion modeling)

## Slide 6: Limitations of Current Neural Codecs
High token rate (long token sequence)
  e.g., 6kbps Descript audio codec has 600 tokens per second
  Make auto-regressive modeling challenging and computational expensive
Poor reconstruction quality at low bit rate (e.g., 0.6 kbps).
  Most previous studies work on bit rate > 2kbps
  Can we go further under 1.0 kbps?
Falling short in capturing semantic information
  For example, latent encodings given by 6kbps achieved an average accuracy of only 33% on the HEAR benchmark, while AudioMAE latent encodings achieved an accuracy of 61% (without finetuning).

## Slide 7: Motivations
  Shorter sequence: Lower token rates at 25, 50, or 100 tokens per second.
  Better reconstruction at lower bit rate: 0.3~1.4 kbps
  Improved semantic in the codec tokens (which potentially can lead to better language modelling)

## Slide 8: SemantiCodec
Ultra-low bit rate (0.31 kbps ~1.40 kbps, token rate 25, 50, or 100 per second) & Strong semantics in the token & Variable vocabulary sizes
https://haoheliu.github.io/SemantiCodec/
CrossAtten
Large scale k-means is challenging
AudioSet + Million Song Dataset + GigaSpeech
https://github.com/haoheliu/kmeans_pytorch
AudioMAE
Encoder

## Slide 9: AudioMAE (Huang et al. 2022)
Self-supervised pretrained ViTs for reconstructing missing mel-spectrogram patches
Meaningful representation of the mel-spectrogram patches

## Slide 10: Why AudioMAE?
AudioMAE has a better structured latent space.
Better represent the semantic of audio for LLM training

## Slide 11: Diffusion Model
Forward Diffusion: Start with real data (or ).
Reverse Diffusion: Train a model to predict from
Markov chain
Diffusion Model Decoder Training
Conditional diffusion distribution in closed form
Diffusion Model Decoder
Derived from the Evidence Lower Bound of
in closed form
Gaussian Identity
Constant

## Slide 12: Latent Diffusion Model (Rombach et al. 2021)
Diffusion modeling in a compressed space
  Less computation
  Better generative modeling
Credit: Latent Diffusion Models: Is the Generative AI Revolution Happening in Latent Space? (NeurIPS 2023 Tutorial)

## Slide 13: Experimental Evaluations
Metrics:
  MEL: Mel spectrogram distance
  STFT: Short-time Fourier Transform Distance
  ViSQOL: Virtual Speech Quality Objective Listener Score
  WER: Word Error Rate
  Accuracy: Audio classification task accuracy
  MUSHRA Scores
Datasets (we only use audio):
  GigaSpeech (10K hours), Million Song Dataset (510K music tracks), MedleyDB (122 tracks), MUSDB18 (10 hours), AudioSet (2M), VGGSound (190K), WavCaps (7K hours)

## Slide 14: Experimental Evaluations
Baselines:
  Encodec (EC): 23M parameters
  Descript Codec (DAC): 74M
  HiFi-Codec (HC): 63M
Evaluations:
  Reconstruction performance evaluation: LibriTTS clean test set (300 speech utterances), AudioSet general sound (500 audio signals), MUSDB18 (50 songs covering vocals, drums, bass, etc.); 1050 audio clips in total
  Semantic information evaluation: HEAR benchmark (NSPitch, ESC-50, LibriCount, CREMA-D, Vocal Imitations (VoImit), Speech Commands(SC))
  Subjective evaluations: MUSHRA test: 10 raters, 10% of evaluation data (25 music tracks, 30 speech recordings, and 50 general sound samples)

## Slide 15: Better Reconstruction Quality

## Slide 16: Better Semantic in the Tokens
Significantly better when using only a single codebook

## Slide 17: Using Multi-semantic-Codebook is Beneficial
Learnable v.s. Frozen Semantic Codebook

## Slide 18: Classifier-Free Guidance Helps, but not a lot.
Cluster ↑  Semantic ↑ / Reconstruction ↑

## Slide 19: Samples Comparison

## Slide 20: Visual Comparison
Better reconstruction with a lower bit rate
Better semantic in the audio token (potentially better Audio LLM?)
https://haoheliu.github.io/SemantiCodec/
Sound demos:

## Slide 21: Demos
https://haoheliu.github.io/SemantiCodec/
More sound demos:
General Audio
(AudioSet)
Original
HiFi-Codec
(2.0 kbps)
Encodec
(1.5 kbps)
DAC
(1.41 kbps)
SemantiCodec
(1.43 kbps)
SemantiCodec
(0.35 kbps)
DAC
(0.47 kbps)
Speech
(Libri)
Music
(MUSDB18)

## Slide 22: Conclusion & Future Work
  We have presented SemantiCodec, which produces audio tokens of more semantic, lower token rate, with thus enabling ultra-low bit rate audio codec, and works for any length audio.
  Future works:
    How does the semantic of audio token related with LM performance?
    Can shortened audio token sequence alleviate LM robustness issue?
    Specialized SemantiCodec

## Slide 23: Acknowledgements
Thanks to Haohe for providing slides.
The project is funded in part by EPSRC and British Council.

## Slide 24: Take Aways
Arxiv Paper: https://arxiv.org/abs/2405.00233
Project Page: https://haoheliu.github.io/SemantiCodec/
Open-source Code: https://github.com/haoheliu/SemantiCodec-inference
Demos: https://haoheliu.github.io/SemantiCodec/